## Slide 1
AKTOR is the construction arm of ELLAKTOR and its biggest subsidiary. It is established as a leading international infrastructure company, providing a wide range of highly diversified services in the fields of Construction, Photovoltaic Parks, Quarry Management, Technical Facilities and Project Management.

## Slide 2
Doha Metro - Gold Line Project
10 No. Underground Stations
24 km TBM Tunnel
Approx. 3 Billion USD Contract
GOLDLINE METRO PROJECT – Doha, Qatar
6x EPB Tunnel Boring Machine 7.15 m
15x MSV with additional Equipment
24 km Conveyor Belt System
3x Grout Mixing Plants
6x Ventilation Systems
All procured from a single manufacturer
in tunnelling industry i.e HERRENKNECHT AG.
Tunneling Solution
AKTOR’s flagship infrastructure project

## Slide 3
Gold Line Metro of Doha in Qatar

## Slide 4
What a TBM looks like?

## Slide 5
3 Technological Domains
EPB - Tunnel Boring Machines (TBMs)
Auxiliary Equipment
Site Installations
‘’Total tunneling solution’’

## Slide 6
Concept of EPB Shield Principle of Tunnel Boring Machine
EPB technology is fundamentally based on the use of the excavated soils as the supporting measure in the excavation chamber.
Classical EPB technology has undergone crucial development during the last 10 years. The classical application range of EPB shields has been extended in cohesive soils as well as the less cohesive soils and mixed geology such as soft ground and rock.

## Slide 7
GROUND GEOLOGY & TBMs - OPEN – CLOSE MODE:-
The main characteristics of the geological formations of the drives described below:
TUNEL HOMOROD - PROFIL GEOLOGIC
Geologically, the Homorod tunnel is pictured as argillaceous marls that are predominantly expected in the alignment which will become a soil-like plastic paste after excavation, In the medium term, the marl behaves convergently. However, it will be stable and can mostly be excavated in open EPB mode.
If necessary (approx. 500 m at the beginning and approx. 500 m towards the end of the advance), it is possible to rapidly change to closed EPB mode in heavily weathered zones.

## Slide 8
GROUND GEOLOGY & TBMs - OPEN – CLOSE MODE:-
The main characteristics of the geological formations of the drives described below:
TUNEL ORMENIS - PROFIL GEOLOGIC
In Ormenis tunnel the weathered mudstones and fault zones, the first 0.5 km should be excavated in closed EPB mode. Approximately 4.0 km of the 5.5 km of the middle section could be excavated in open mode with belt discharge, and the last 0.5 km again in closed EPB mode. However, considering the trachyte zone (medium to hard rock) we selected a rather classic EPB TBM but Hard rock oriented cutterhead design, which can react more flexibly driving through soil conditions and at the same time able to pass through more rocky material and face any event of unforeseen fault zones.

## Slide 9: TBM Parameters
Screw Conveyor Dia.: 1150 mm
Breakout torque: 22103 kNm
Max operating pressure (on axis): 3,0 bar
  Total TBM length: 105 m
  Max rotation speed: 4.1 RPM
Maximum thrust force: 84736 kN (19 Double)
Main Drive Electrical power: 3600 kW (200 kW x 18)
Primary Voltage: 20 kV
Excavation Diameter: 9.8 m
Center – Double Disc cutters: 4 No
Face – Single Disc cutters: 38 No
Gauge – Single Disc cutters: 15 No
Scrapers: Approx. 108
Buckets lips: 8+8 No

## Slide 10
TBM INFORMATION SYSTEMS
Guidance System / TUnIS Navigation TBM Laser (VMT)

## Slide 11
TBM – Tunneling System:

## Slide 12
TBM Assembly :

## Slide 13
TBM Screw Conveyor photo
TBM – Tunneling Equipment Transport:

## Slide 16
TBM Breakthrough in a Metro Station

## Slide 17: Tunnel Belt Conveyor System
The belt conveyor system is solely intended for the removal of the excavated materials from the TBMs to the discharge point (Muck pit) with great precision, without affecting the Tunnel logistics (Segments transport, Tunnel consumables, Tunnel utilities, etc.), therefore replacing the conventional technology of Locomotives or muck wagons.
Seamless interface to the TBM.
Removal of the excavated material adjusted to the tunnelling speed.
Low personnel requirements through automated processes.
Belt conveyor systems are high-tech systems, keeping the risk of accidents to the minimum level.
Safety is also ensured even when driving along curves with a tight radius.

## Slide 18
Tunnel belt conveyor Overview:

## Slide 19
Tunnel belt conveyor on gantry :-

## Slide 20
Continuous Tunnel Belt Conveyor System

## Slide 21: Discharge belt conveyor

## Slide 22: MSV (Multi Service Vehicle):
The scope of the MSV were to feed the segments into TBM.
The MSV was constructed according to state-of-the-art standards and generally accepted technical safety regulations. It has the capacity to carry a set of one ring ( 6+ 1 ) along with the consumables .
MSV has the provision to mount below attachments
Personnel module (capacity of 20 persons )
Equipped with Safety system for rolling on super elevation
Material platform module

## Slide 23
MSV Technical Data:
MSV 50 – 4 driving wheels -8 wheels-maxi Load capacity 45 t Multi service vehicles, heavy duty, self-propelled on tires 4x8x8, Diesel-powered, double cabins
Dimensions and performance
Width at the power pack 1,540 mm
Height of the power pack 2,648 mm
Length MSV 50 Refurbished 18,900 mm
Weights Tare weight Approx. 18,000 kg
    Payload 45,000 kg
    Maximum vehicle weight Approx. 63,000 kg
    Power group Certified motor for European regulations
    STAGE 3 (2015) Engine power 200 kW
    Water cooling
    Hydraulic power Main pumps: hydro translation
Safety equipment
Security system for rolling on super elevation
Consisting of an alarm and stop inclinometer installation, mounted on each vehicle.
Signals equipment Orange flashing lights
    2 x 2 head lights in forward and backward direction
    2 x 2 red lights for driving forward and backward
    Buzzer forward and reverse gear

## Slide 24
MSV (Multi Service Vehicle) :
Transportation on site

## Slide 25
MSV (Multi Service Vehicle) :

## Slide 26
MSV (Multi Service Vehicle) lifting photos

## Slide 27: Containerized Modular Grout Mixing Plant:

## Slide 28: Grout Mixing Plant
The Containerized Modular Grout Mixing Plant is designed to automatically prepare a grout mix component A (water, cement, bentonite and additives) and transfer it to the grout injection system located on the TBM . Grout mixing plant is capable of batching and injecting low density grout mixture, maintaining precise control over grout quality at the placement location. State-of-the-art equipment results in high quality backfill concrete .
CONTAINER HOUSING GROUT SHEAR MIXER:- No.1 Specifically Designed 20’ Container, certified for marine transport, housing No.1 Shear mixers equipped with a built--‐in weight batching system for mixing up to three dry components And three additives with water including microprocessor based Integrated Control System suitable to manage manual/automatic operation.
N. 02 Mixer tanks MTW2500
Tank max working capacity: 2.500 lt./each
Each tank equipped with N. 02 Open impeller pumps
2.000 lt/min max. flow rate EACH at MAXIMUM 2 bar,
4.000 lt flow rate each tank
8.000 lt flow rate total

## Slide 29: Grout Set up - Pipes and FO Cable between TBM and mixing plant

## Slide 30: Grout Mixing Plant– B component:
4 x Transfer Pump Component B inside container - Description of the pump:
- 5” double effect piston / 8” stroke
- 90 Bar max. pressure / 150 lt/min. max flow rate; electro-hydraulic
- powered, with 7,5 kW electric motor
- control panel with: stroke counter, hand grips to regulate the pressure and the grout flow rate, main
- electrical switch, hydraulic oil pressure gauge, grout pressure gauge, automatic/manual switch, on/off button, emergency stop button.

## Slide 31: Grout Mixing Plant – Silos Set up:

## Slide 32: Ventilation Axial Flow System
Ventilation System :- During the tunnels excavation, it is necessary to continuously keep the Tunnel well-ventilated, ensuring an adequate fresh air flow for the personnel working inside the tunnel. In Brasov Lot 2 Rail project , the ventilation system has been designed to comply with the following requirements prescribed by the BS 6164:2011 Standards. Below are the details of the Ventilation fan selected for the said project .
Axial Flow Fan: Inner Diameter: Ø 1200 mm
Motor Power: 2 x 75 kW
Rotation Speed: 1500 rpm
Voltage: 400/50 V/Hz
Inlet Nozzle: Inner Diameter: Ø 1200 mm Complete with protection mesh:
Silencer: Quantity: 02 unit
Frequency Inverter: Quantity: 01 unit for motor power with: 150 kW
Voltage: 400 V - 50 Hz

## Slide 33
Tunnel Portal - Main Site Installations

## Slide 34
Tunnel Portal - Temporary segment storage area

## Slide 35
Site Installation – Storage Area

## Slide 36
Portal Area - Grout Mixing Plants

## Slide 37
Portal Area - TBM Launching

## Slide 38
Portal Area - TBM Launching and TBM assembling in parallel

## Slide 39
VA MULTUMIM PENTRU ATENTIE !